## Slide 1: GPON Training
11/2016

## Slide 2: Agenda
GPON Technology
CLI Service Provision
Element Management System
New ONT Model Introduction
New Firmware Improvements

## Slide 3: GPON Technology
01

## Slide 4
GPON Technology
  What is PON?
  Why PON?
  What are the benefits?
  What is GPON?
  GPON standards
  GPON upstream
  GPON terminology
  GPON DBA
  T-CONT Types
  Upstream QoS
  Downstream Rate Limit
  Relationship between T-CONT Type and Bandwidth Type
  Power Budget
Notes: Power Budget = Estimacion de Potencia.

## Slide 5: What is PON?
PON is one kind of passive optical network with one point to multipoint fiber structure for last mile.
PON consists of:
    Optical Line Terminal (OLT),
    Optical Network Termination (ONT), and
    Passive Optical Splitter.
Notes: What is the PON?
The fiber-to-the-home (FTTH) architecture has been considered an ideal solution for accessing the networks, because of the huge capacity, small size and lightness, and immunity to electromagnetic interference of optical fibers.

## Slide 6: Why PON? (1/2)
Increasing Bandwidth Demands.
Ideal solution for stable networks.
  Immune to electromagnetic interference.
Reduce the number of lasers.
Current Last mile constrains the bandwidth delivery to customer.
xDSL Bandwidth Bottleneck.
Metro Backbone
CO
Notes: Why the PON?
The increase of services (E.g. HD streaming video) has prompted more bandwidth demands by fiber.
Generally, the last mile network access has always constrained the bandwidth delivery (as in the case of xDSL technology, latest developments VDSL can reach up to 200Mbps and G.Fast up to 1Gbps at 100M).
The introduction of the PON solves many of those problems with the cost-down deployment and more bandwidth delivery.

## Slide 7: Why PON? (2/2)
Notes: Why the PON?
In order to achieve the fiber network to home, in the past, the straightforward way to deploy the optical fiber in the local access network is to use a point-to-point (P2P) technology with dedicated fiber running from the CO to each end user subscriber (Fig. A). This is a simple architecture, however in the most cases its too expensive, because it requires significant outside fiber plant deployment and connector termination space in the local exchange. Considering N subscribers at an average distance L km from CO, a P2P design requires 2N transceivers and N x L total fiber length.
To reduce fiber deployment, it is possible to deploy a remote switch or concentrator close to the neighborhood. This will reduce the fiber consumption to L km, but will actually increase the number of transceivers to 2N+2, as there is one more link added to the network (Fig. B). In addition, a curb-switched network architecture requires the electric power as the backup power at the curb switch. Currently, one of the most significant operational expenditures for xLECs is that providing and maintaining the electric power in local loop. Therefore, it is logical to replace the hardened curbside switch with an inexpensive passive optical splitter.
A Passive Optical Network (PON) is a technology viewed by many as an attractive solution to the first-mile problem. A PON minimizes the number of the optical transceivers, CO terminations and fiber deployment. A PON is a point-to-multipoint (P2MP) optical network with no active elements in the signals’ path from source to destination. The only interior elements used in the PON are passive optical components, such as the optical fiber, splices, and splitters. An access network based on a single-fiber PON only requires N+1 transceivers and L km of fiber (Fig. C).

## Slide 8: What are the benefits?
gpon
xDSL
gpon
VoIP
IPTV
HSI
Stable Network
More Bandwidth
More Services
Lower Costs
Notes: More stable networks as it is not affected by electromagnetic interference compared to copper.
Bandwidth can reach Gigabit speeds in long distances.
More services can be carried like Internet, IPTV, VoIP, data. FTTH deployment is getting more popular. Fiber can be extended to the home, even to old building which originally relied on xDSL technologies. Therefore, the operator can consider using the FTTH to replace the existing xDSL.
Lower costs due to the reduced capex cost, and higher bandwidth can be delivered to customers at farther distances. Due to “Passive fiber-optic components”, the user doesn’t need to add power input into the splitter It means: the ODN network can be built anywhere.

## Slide 9: What is GPON?
GPON stands for Gigabit Passive Optical Networks.
It can support for Ethernet, ATM and TDM (PSTN, ISDN, E1 and E3) traffic.
Defined by ITU-T G.984 series.
Notes: International Telecommunication Union (ITU)-Telecommunication Standardization Sector(T).
Asynchronous Transfer Mode (ATM).
Time-Division Multiplexing (TDM).
Public Switched Telephone Network (PSTN).
Integrated Services Digital Network (ISDN).
E1 (or E-1) is a European digital transmission format devised by the ITU-TS.
E3 (E-3) carries 16 E1 signals with a data rate of 34.368 million bits per second.
Gigabit-capable Passive Optical Networks (GPON).

## Slide 10: GPON Downstream
Use Broadcast to be the method for GPON downstream data transmission.
Support AES (Advanced Encryption Standard) method.
Notes: Use broadcast method for downstream, all of the ONU can receive the same data, but distinguish the data for different ONU by each ONU ID, ONU can only receive its own data through this filtering way. AES encryption is used to prevent eavesdropping.
Continuous mode operation.
Downstream data will be broadcast to all ONTs in the same PON. Everyone ONE will provide one unique ONT-ID.
Support AES (AES – Advanced Encryption Standard) method.
1 nanosecond =1.0 × 10-9 seconds.

## Slide 11: GPON Upstream
Use TDMA (Time Division Multiple Access) to be the method for GPON upstream data transmission.
Dynamic Bandwidth Allocation (DBA).
Notes: The uplink be divided into time slots , according to the upstream bandwidth map string found in the downstream frame to assign each ONU uplink time slot , thus all ONUs can follow a specific order to send/receive its own data, will not have conflict in order to compete with the time slot.
GPON upstream:
TDMA – Time Division Multiple Access
Burst mode operation
ONTs will send upstream by TDMA method in the same media. Everyone ONT could be allowed to transmit the data in assigned time slot.
DBA. The OLT will monitor the transmission of the ONT every time to check for efficiency and dynamically adjust the assignment of time slots for the ONTs in the next transmission. The frame of downstream to ONT will include the time slot information in last upstream transmission of ONT.

## Slide 12: Traffic Class to Queue Reference 2
Notes: Priority= Diferentes redes dentro de una misma empresa (wifi invitados, red gerencia, red administración)
Sobredimensionaminento de ancho de banda (tenemos 40 megas pero podemos venderle a los clientes paquetes de 100 megas)
Millas de acceso sólo en capa 2 (MAC tabla de MAC) más de 32000 usuarios base de datos tan grande realentizaría el servicio (notaríamos retraso). Equipos de agregación sólo en Nivel Mac (capa 2) switches, olt, dslam, etc.
En esta dispositiva hay una traducción de capa uno a capa dos (prioridades) con la capa 1 (encendido y pagado del laser de la ONT).

## Slide 13: GPON DBA
Dynamic bandwidth allocation takes advantage of several attributes of shared networks:
  all users are typically not connected to the network at one time
  even when connected, users are not transmitting data (voice or video) at all times
  most traffic occurs in bursts -- there are gaps between packets of information that can be filled with other user traffic.
Notes: SIR: Sustained Information Rate. (Usado VoIP)
AIR: Assured Information Rate. (Usado Video, Vigilancia)
PIR: Peak Information Rate is same as Excess Information Rate(EIR) . (Usado en Internet)
Fixed BW: Reserved upstream BW, cyclically allocated regardless of demand.
Assured BW: Similar to fixed, but BW may not be given without demand.
Non-Assured: Bandwidth only given if BW is available but not guaranteed.
Best Effort: Demand only met if remaining upstream BW is available.
Se analiza matematicamente el tiempo y necesidades de transporte de información en función de la carga que tenga el buffer de la ONT, es decir, si una ONT tiene el buffer lleno o por llenarse, priorizaremos ese transporte de datos para evitar pérdida de paquetes.

## Slide 14: T-CONT Types (Upstream QoS)

## Slide 15: Upstream QoS (2/2)
DBA will be based on T-CONT types to ensure that total of bandwidth rate does not exceed the maximum of PIR.
Total MAX. rate is 1.25G for upstream.
Notes: Committed Information Rate (CIR) is minimum bandwidth that is guaranteed to work under normal conditions, at any time the bandwidth should not fall below.
Peak information rate (PIR) is burstable bandwidth.

## Slide 16: Downstream rate limit
Total MAX. rate is 2.5G for downstream
Downstream rate limit can be applied in OLT or ONT.
  ONT can set bandwidth rate limit per gem flow.
  OLT can set bandwidth rate limit per:
    gem flow, or
    gem flow + per ONT.

## Slide 17: Relationship between T-Cont type and Bandwidth type
Notes: SIR: Sustained Information Rate is same as Committed Information Rate (CIR).
  AIR: Assured Information Rate.
PIR: Peak information rate is same as Excess Information Rate (EIR).

## Slide 18: Power Budget (1/2)
Splitter attenuation
Loop attenuation
Connector attenuation
Splitter Type | 1:2 | 1:4 | 1:8 | 1:32
Attenuation | ≤ 3.5 dB | ≤ 7.0 dB | ≤ 10.5 dB | ≤ 17.5 dB
Loop distance | Per Km
Attenuation | ≤ 0.5 dB
SC Connector | Per Connector
Attenuation | ≤ 0.3 dB
Notes: Attenuation is the gradual loss in intensity of any kind of flux through a medium.
SC is a snap-in connector as shown in the image
PC stands for polished connector (PC, UPC – ultra-polished, APC – angle polished)

## Slide 19: Power Budget (2/2)
Notes: Power Margin = The power margin is the difference between available signalpower and the minimum signal power needed to overcome system losses

## Slide 20: Any Question?
01